## Slide 1
Regional Framework and Controls on Jurassic Evaporite and Carbonate Systems of the Arabian Plate
CHRISTOPHER G. ST.C. KENDALL
University of S. Carolina
kendall@sc.edu

## Slide 2: Acknowledgments
University of South Carolina
&
E.A.G.E.
I extend my thanks & appreciation to:
for helping make this presentation possible
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 3: South Tethyan Margin
Northeastern flank of Gondwanaland from Arabian Plate through Zagros & Taurus Mtns, Levant & N Africa
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 4
Presentation Outline
Carbonate
Plays
Evaporite
Settings
Evolving Basins
& Plates
Basin Phase Evolution =
Plate Tectonic Setting +
Subsidence Mechanism
Talk based on Proven Plays from Commercial Databases (e.g., C & C Reservoirs, IHS Energy, USGS Assessments)
Carbonate/Evaporite Hydrocarbon Reserves
Tie between Carbonate/Evaporite Settings
  Climate
  Basin Phase (extension, compression, or barred)
  Sea Level
Carbonate/ Evaporite Play Geometries
Summary & Conclusions

## Slide 5
Unconventional Plays may double current conventional reserves
(1) USGS World Assessment (2000)
(2) hMobil CATT Study (1999)
56%World Total Reserves in Carbonates
56% Total Reserves in Carbonates
Total
Reserves
Carbonate
Fraction
0
1
2
3
4
5
World
Total (1)
Trillions BOE
4.1
2.3
DISCOVERED CONVENTIONAL
Proven Conventional Plays with Discovered
Reserves - Reported (764,000 MBOE)
64%
36%
Carbonate Play Association with Evaporite Seal: N = 31
Carbonate Play Association with No Evaporite Seal: N = 45
Weber & Sarg, 2005
Total in
Carbonate
Fields (2)
Significance of Carbonates & Evaporites
“Conventional Plays”
Database captured 33% of total discovered reserves in carbonates
41% of plays exhibit an evaporite seal
64% of discovered reserves trapped under an evaporite seal
So evaporites are important?

## Slide 6
Paleozoic
Jurassic
{
Cretaceous
{
Tertiary
Location of Oil & Gas Fields of Arabian Gulf - Reservoirs are Younger to East
Most are carbonate plays that accumulated beneath evaporite seals in inter-plate isolated restricted basins, shale forming a major seal in the Cretaceous

## Slide 7
Carbonate/ Evaporite
Settings
Controls Carbonate Platform Architectural Elements
Evolving
Paleogeography, Basins &
Plates
Carbonate
Play Geometry
Eustasy
Climate

## Slide 8
Controls on Carbonate Accumulation

## Slide 9
Source Rock Potential

## Slide 10
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 11: Paleozoic Sediments
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate
Paleozoic landward dominantly siliciclastic continental to fluvio-deltaic & glacial sediments while seaward shales & carbonates more common
Oil fields probably sourced from organic rich mfs events
These same organic rich sediments associated with reservoir quality rocks high grade the hydrocarbon potential of these rocks

## Slide 12: Pre-Cambrian
After Christopher Scotese
Windward Margin
Salt Basin
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 13: Cambrian
After Christopher Scotese
Windward Margin
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 14: Ordovician
After Christopher Scotese
Windward Margin
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 15: Ordovician Glaciation
(after Scotese et al., 1999; Sutcliffe et al., 2000; Le Heron, et al, 2004)
Blue arrows indicate direction of ice sheet advance
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 16: Silurian
After Christopher Scotese
Windward Margin
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 17: Devonian
After Christopher Scotese
Collisionn Margin
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 18: Early Carboniferous
After Christopher Scotese
Collisionn Margin
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 19: Late Carboniferous
After Christopher Scotese
Collisionn Margin
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 20
After Sharland et al, 2001

## Slide 21: Paleozoic Sediments
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate
Paleozoic landward dominantly siliciclastic continental to fluvio-deltaic & glacial sediments while seaward shales & carbonates more common
Oil fields probably sourced from organic rich mfs events
These same organic rich sediments associated with reservoir quality rocks high grade the hydrocarbon potential of these rocks

## Slide 22: Plate tectonics & hydrocarbons Permian, Jurassic & Cretaceous examples
Mesozoic deposition in tropical settings on the lea shore of the extensional passive Tethyian margin favored organic sequestration
Late Cretaceous to Tertiary was a foreland basin flanking the Zagros and Taurus uplift.
Deposition on North African plate occurred in tropical settings, and followed an extensional passive margin
Late Cretaceous it changed to a dominantly compressional margin with localized wrench margins.
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 23
Permian Khuff
Saudi Arabia
Kuwait, Iran
& UAE
Gondwanaland
Tethyan Margin
Notes: 23

## Slide 24: Evaporites - Tectonic Phase, & Source, Reservoir, & Seal, & Sea Level
Major carbonate/evaporite successions from arid tropics adjacent to continental plate margins at start of extensional & end of compressional Wilsonian phases of plate motion & lee of structural & depositional barriers on trailing margins
Juxtapose source, reservoir, & seal, favoring hydrocarbon exploration & exploitation
Geometries of hydrocarbon prone carbonate/evaporite successions are determined by position of base level change
Evidence comes from plate motion cycles of Arabian Gulf, Central Asia, Atlantic, Cordilleran & Appalachian Mountains
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 25: restricted basin evaporites
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 26
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate
Permian - Structural Barred Basin - Arabian Gulf
lea shore
arid-tropical air system
some shadow from adjacent continents
juxtaposed source seal and reservoir
SOUTH
TETHYS
SWEET
SPOT
Permian Khuff
Saudi Arabia
Kuwait, Iran
& UAE
structural &
depositional
barrier over
exotic
terrains
confined
seaway

## Slide 27
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate
Example of Barred Basin Mesozoic - Arabian Gulf
lea shore
arid-tropical air system
some shadow from adjacent continents
juxtaposed source seal and reservoir
SOUTH
TETHYS
SWEET
SPOT
Upper Jurassic
Saudi Arabia
Kuwait, Iran
& UAE
structural &
depositional
barrier over
faulted margin
horst blocks
confined
seaway

## Slide 29: low stand evaporites

## Slide 30: transgressive evaporites

## Slide 31: high stand evaporites

## Slide 32: Restricted Basins Isolated by Build Up Barriers Organic Rich Fill Arabian Gulf Jurassic
After Fox & Albrandt,2002
Gotnia Basin
Arabian Basin
South Arabian Basin

## Slide 33
Cretaceous Paleogeography
After Peter Skelton
lea shore
humid-tropical air system
some shadow from adjacent continents
juxtaposed source seal and reservoir
SOUTH
TETHYS
SWEET
SPOT
Cretaceous
Saudi Arabia
Kuwait, Iran
& UAE
confined seaway

## Slide 34: Collision Margin Evaporites
restricted
entrance
to sea
isolated linear
belt of interior
drainage
regional
drainage
into basin
arid tropics air system
wide envelope of surrounding continents
SWEET SPOT!
juxtaposed source
seal & reservoir

## Slide 35
After Sharland et al, 2001

## Slide 36: Evolution of Arabian Shield - Tectonics
Foreland Basin
Compression &
Foreland Basin
Extensional margin
Extensional margin
Interior Sag

## Slide 37
Geologic Cross-Section - Arabian Gulf
Accommodation produced by low frequency tectonic subsidence modulated by higher frequency eustatic changes in sea level and varying rates of sediment accumulation

## Slide 38
Geologic Cross-Section - Arabian Gulf
Relatively flat-lying assemblages of Paleozoic, Mesozoic through Cenozoic interbedded carbonates, evaporites and clastic horizons

## Slide 39
Geologic Cross-Section - Arabian Gulf
Paleozoic landward dominantly siliciclastic-continental to fluvio-deltaic & glacial while seaward shales & carbonates

## Slide 40
Geologic Cross-Section - Arabian Gulf
Mesozoic exposed areas updip to west over stable shelf while dominantly carbonate on shelf and intraplate basins eastward on “unstable” shelf

## Slide 41
Geologic Cross-Section - Arabian Gulf
Oil fields are younger from west to east, Paleozoic stratigraphy caps Precambrian in almost all Southern Tethys with exceptions that include the Burgan Arch (Kuwait), or Sirte Basin (Libya)

## Slide 42
Jurassic Evaporite and Carbonate Systems of Arabian Plate
Gas
Oil
Mesozoic Oil & Paleozoic Gas

## Slide 43: Controls on the Petroleum Systems of the Southern Tethys
Petroleum Systems function of:-
Plate position
Malenkovitch driven climate, eustasy and oceanography
Organic productivity & preservation
Sediment character
Structural and thermal history
Many of these factors dependent on others
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 44: The Hanifa Formation Stratigraphic Framework
Each formation was deposited as a complete 3rd order sequence
Source
Reservoir
Seal
Notes: This chart shows the third order eustatic cycles (red) super-imposed on the lithostratigrahic section.
Each formation corresponds to a complete 3rd order cycle.
The Hanifa Formation (blue highlight) is positioned in the transgressive limb of the 2nd order eustatic cycle (blue line).

## Slide 45: Carbonate/Evaporites Plays & Sequence Stratigraphy
Downdip restricted playas, salinas & basin evaporites (upper surface coincides with sea level position of the lowstand (LST) & following transgressive (TST) system tracts
Updip supratidal sabkha evaporite cycles (upper bounding surface preserved in regressive coastlines matching sea level position of late high stand (HST) system tract

## Slide 46
Continental
Evaporites
Platform Evaporites
Basin-Center Evaporites
Mean Sea Level
Sabkha, Salina,
Mudflat
Subaqueous Evaporative Lagoon
Shallow to
Deeper Basin
Basin
Center
Platform
Discovered Reserves for Proven Carbonate Plays
Total = 490,000 MBOE
Discovered Reserves for Proven Evaporite Plays
Total = 485,884 MBOE
52%
48%
Major Evaporite Settings
Platform (Commonly product of LST & TST)
  < 50 m thick evaporite intervals, commonly < 5 m thick evaporite beds inter-bedded with thin to thick carbonate intervals
  Shallow water (Evaporitive Lagoon) & subaerial (Sabkha, Salina, Mudflat) evaporites landward of barrier or sill
  Open marine sediments deposited seaward of sill
Basin-Center (Commonly product of LST & TST)
  Thick evaporites deposited across whole basin (> 50 m thick evaporite intervals)
  Shallow to deep water evaporites occur in many different settings (shelf, slope, basin)
Continental (Playa Lakes) (not discussed here)

## Slide 47
Evaporite Setting Plays & Basin Phase Evolution
Play Elements & Tectonic Evolution Pathway for Passive Margin Settings
Rift
Foreland
Drift
Plays Occur in Passive Margin Settings
25% of Plays Do Not Evolve to Foreland Phase
Stratigraphic Traps are Important
Source, Reservoir, Seal Likely in Drift Phase
>90% Source Rocks Carbonate in Origin
Source Rocks in Close Proximity to Reservoir
Sag
Kendall - Jurassic Evaporite and Carbonate Systems of Arabian Plate

## Slide 48: Conclusions
Hydrocarbons trapped in fields in relatively horizontal Paleozoic, Mesozoic through Cenozoic sediments of Tethys southern margin
Fields can be analyzed and characterized in terms of Wilsonian cycles of plate drift that control:
  Low frequency Tectonic movement
  2nd and 3rd order eustatic Malenkovitch driven changes
  Sediment supply and organic matter sequestration
Analysis of South Tethys margin high-grade evaporite-carbonate hydrocarbon plays with great potential are abundant

## Slide 49
Conclusions
Now let’s
find oil!

## Slide 50: Middle East - Approximate Reserves
Saudi Arabia 263.5 bbls 204.5 Tcf
Iraq 112.0 bbls 109.0 Tcf
UAE 97.8 bbls 212.0 Tcf
Kuwait 96.5 bbls 52.7 Tcf
Iran 89.7 bbls 812.3 Tcf
Oman 5.3 bbls 28.4 Tcf
Yemen 4.0 bbls 16.9 Tcf
Qatar 3.7 bbls 300.0 Tcf
Syria 2.5 bbls 8.5 Tcf
Bahrain 0.1 bbls 3.9 Tcf
Crude Oil(BB) Natural Gas (TCF)
Most in carbonate plays beneath evaporite seals

## Slide 51
Climate, Eustasy, & Source Rock Potential

## Slide 52
Most Arabian Gulf fields are carbonate plays beneath evaporite seals in restricted basins juxtaposing source, seal and reservoirs
Paleozoic
Jurassic
Cretaceous
Tertiary
Arabian Gulf fields become
younger
to east

## Slide 53: Low Stand Evaporite Signals
sequence
boundary

## Slide 54: Transgressive Evaporite Signals
transgressive
surface

## Slide 55: High Stand Evaporite Signals
maximum
flooding
surface

## Slide 56
Previous discoveries in Levantine Basin - zero
Undiscovered reserves – recent & exciting discovery in lower Miocene subsalt at Tamar of 5 tcfs gas in the Levantine basin
Great implications for offshore all of North Africa

## Slide 57: Conclusions
South Tethys margin is the world’s premier hydrocarbon producing area, best in the Middle East, good in Africa and promising in the Levant, Syria and Turkey
Analysis of South Tethys margin suggests hydrocarbon plays have great potential and are abundant and similar to current fields

## Slide 58: Carbonate Platform Accommodation
ecological accommodation
physical accommodation only

## Slide 59
CI
EX
Evaporite Setting Plays & Basin Phase Evolution
N = 9 Plays
Play Elements & Tectonic Evolution Pathway for Passive Margin Settings
Rift
Sag
Foreland
Drift
Pelagian
Rift
Sag
Drift
Foreland
Post-Seal
Seal
Reservoir
Source
Post-Seal
Seal
Reservoir
Source
Post-Seal
Seal
Reservoir
Source
Passive Margin
TECTONIC PHASE FOR PLATFORM-SUBAQUEOUS
SALTERN EVAPORITE SETTINGS
Continental Interior
Back-Arc
Peten
Arabian Platform
Timan-Pechora
Angara-Lena
Gulf Basin
Dominant Occurrence
Minor Occurrence
Plays Occur in Passive Margin Settings
25% of Plays Do Not Evolve to Foreland Phase
Stratigraphic Traps are Important
Source, Reservoir, Seal Likely in Drift Phase
>90% Source Rocks Carbonate in Origin
Source Rocks in Close Proximity to Reservoir
~
~
~
~
~
~

## Slide 60
N = 13 Plays
Play Elements & Tectonic Evolution Pathway for Continental Interior Settings
Rift
Sag
Foreland
Evaporite Play Settings & Basin Phase Evolution
Rift
Sag
Drift
Foreland
Post-Seal
Seal
Reservoir
Source
Post-Seal
Seal
Reservoir
Source
Post-Seal
Seal
Reservoir
Source
Passive Margin
TECTONIC PHASE FOR BASIN CENTER-SHALLOW
MARINE SHALLOW BASIN EVAPORITE SETTINGS
Continental Interior
Back-Arc
Gulf Suez
Michigan
Oman Salt
European Permian
Williston
Dnepr/Donets
Pripyat
Paradox
Zagros Fold Belt
Amu Darya
Western Canada
Dominant Occurrence
Plays in Continental Interior Settings
40% of Plays Do Not Evolve to Foreland Phase
Stratigraphic Traps Important
Source, Reservoir, Seal Possible in ALL Phases
>90% Source Rocks Carbonate in Origin
Source Rocks in Close Proximity to Reservoir
Minor Occurrence

## Slide 61
Summary & Conclusions
~
~
~
~
~
One can predict Carbonate Play Opportunities in Evaporite Basins from an understanding of Basin Phase Evolution and Evaporite Setting
The opportunities occur in:
Land Detached Isolated Platforms in Basin-Center Evaporite Settings in Arc-Related and Passive Margin Settings that Evolve to the Foreland Basin Phase
Isolated buildups in Platform Evaporite Settings in Passive Margin Settings That May or May Not Evolve to the Foreland Basin Phase
The Exploration potential of Carbonate Plays in Evaporite Basin is good. However where the “prospects” are located is the ever evolving objectives tied to access to prospective acreage and a drilling program!